## Slide 1
CAPSTONE PRESENTATION
What Regulating Trucks through Glenwood Canyon Achieves — and Does Not
Jon Stavney
UC Denver | School of Public Affairs
Spring 2026 | Instructor: Prof. Todd Ely
Client: I-70 Coalition
May 1, 2026
Notes: Thank you. Grateful for the opportunity.
Learned a lot, still learning as I prepped for this call. Could have put much more time in - full year? Hard to imagine putting more time in than I did this semester – most weekends and some weekdays.

## Slide 2
University of Colorado Denver, School of Public Affairs, MPA.
Capstone Process
Glenwood Canyon, photo by author
Complete Coursework
I began 3 Years ago. In August of 2023I was accepted to the Executive Program, just before start of classes. Honored CPM credits.
Select Client and Topic
Each MPA student completes a Capstone project. It is a Client-Driven process, to find a real-world problem to apply analysis skills learned in the program
Capstone Semester
SPA selects two Capstone Professors. Student then identifies a Second Reader. Through multiple assignment, she builds up to the project – Prospectus, Literature Review and preliminary Methodology, May paper complete.
Presentation
An On-Line oral presentation is required with Client, Prof and Second Reader, as is a Final Capstone Paper. I am scheduled to present to I-70 Coalition later this year.
I chose this project because it was interesting, not too close to my work. The topic was a late call stemming from a discussion at the January I-70 Coalition Meeting, a stretch for me statistically, local, out of my wheelhouse professionally, but had contacts with access.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
2 / 17
Notes: The canyon is crucial with complex engineering.
A unique segment to study. Different road geometry than most of rural I-70 – bridges, tunnels, tight curves, limited shoulders.
Contained, well monitored – 128 cameras. Good crash data.
Of great interest, NWCCOG participated in update to Denver Metro Chamber of Commerce I-70 Congestion study – quoted in draft. Note that these numbers are related to closures vs crashes.

## Slide 3
I-70 through Glenwood Canyon
An economic lifeline and an engineering marvel — and a chokepoint
Glenwood Canyon, video by author
12.5 mi
of constrained, multi-curve canyon
$2 M
estimated cost to the state per closure hour
$2.3 M
tourism transactions per workday hour
in the mountain resort region
1 of 4
east–west routes between Canada and Mexico
Only paved route through several Western Slope counties — closures impact regional transportation networks
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
2 / 17
Notes: The canyon is crucial with complex engineering.
A unique segment to study. Different road geometry than most of rural I-70 – bridges, tunnels, tight curves, limited shoulders.
Contained, well monitored – 128 cameras. Good crash data.
Of great interest, NWCCOG participated in update to Denver Metro Chamber of Commerce I-70 Congestion study – quoted in draft. Note that these numbers are related to closures vs crashes.

## Slide 4
The Problem: Truck Crashes, Long Closures
Winter 2022–2023: dramatic crashes seized public attention
January 2023
Six consecutive truck wrecks closed the canyon in a single month
Tanker spill
3,000 gallons of fuel spilled, prolonging closure and cleanup
Multi-hour closures
Closures up to 12 hours rerouting traffic 3–4 hours through state highways
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
3 / 17
Notes: VERY DRAMATIC: Appendix XI p. 48
The push to focus on trucks and eventually institute Truck Lane Restrictions emerged from an especially harsh winter.
This was part of the Capstone B – policy story that was extracted.
Regression background revealed that 67% of truck crashes in study period occurred on dry roads (only 12.4% on snowy roads), bu these were the most dramatic, captivating pubic awareness.
Will see that trucks are disproportionately involved in crashes during the study period (23.7%) in relation to traffic (13.4%)

## Slide 5
Research Question & Project Client
RESEARCH QUESTION
Did truck lane restrictions reduce crashes, contributing to the desired outcome of fewer closures?
Quasi-experimental before/after analysis using CDOT crash and traffic data, 2022–2025.
CLIENT
The I-70 Coalition
Founded 2004 by 28 local governments via IGA; now a 501(c)(3) non-profit
Mission: advocate for improvements on the I-70 mountain corridor through joint public–private transportation management
Convenes CDOT, CSP, industry, legislators, and local jurisdictions
Promoted SB24-100, codifying TLR in state law
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
4 / 17
Notes: Research Process is worth a step back. Key secondary source – Crash data, then Closure data.
Literature didn’t address closures. Did cover crashes and the treatment applied in detail.
Chased a policy development story – Client exists in a very policy-focused setting. Legislation came from this CDOT experiment. It took half the semester to set aside with close edits from Prof. Ely making that obvious. Lost a weekend to this.
Could have done a qualitative study interviewing drivers, CSP officers, CDOT personnel on whether canyon felt safer after TLR, then compared that to crash data. Much larger project than Capstone.

## Slide 6
Literature Review: Two Streams of Research
Both inform what we know about truck lane restriction strategies (TLRS)
MODELING STUDIES
Computer simulations across thousands of scenarios
Optimize traffic flow; measure speed, throughput, conflict potential
Newer field, increasingly refined as computing power grows
Surrogate measures (time-to-collision, lane changes) substitute for rare crash events
CRASH DATA STUDIES
Direct study of actual crash events
"Gold standard" — directly correlated to fatality, injury, property damage
Place-specific; supports CDOT's Level of Service of Safety (LOSS) maps
Limitation: low frequency of crashes weakens statistical power at site level
This project draws primarily from crash data analysis, while leveraging insights from the modeling literature.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
5 / 17
Notes: This distinction was important – separating study of approaches to crash (conflict) prevention, vs actual crashes. Most lit from Modeling, but most of the data built from Crashes – even the Closure data.
Didn’t dwell on this, but the most recent Modeling studies also point to monitoring systems that would be real-time, preventative and with much more precise data – actual driver behavior, direct causation. Direct prevention.

## Slide 7
Modeling Studies: Key Findings
Why the literature supports separating trucks from other vehicles
1
Lane separation reduces conflict
Park (2024): Among all interventions, "lane separation by vehicle type" had the greatest impact on truck crash reduction.
El-Tantawy (2009): Restricting trucks from the fastest lane on a 3-lane freeway most consistently reduced conflicts.
2
Lane changes create a potential for vehicle conflicts
Ma (2023): Approximately 75% of traffic accidents stem from driver lane-change errors.
Reducing oscillation and shock waves from lane changes is a core pathway to safety.
3
Speed homogeneity matters
Choi (2014): Truck lane restrictions "make the traffic stream more homogeneous" — speed variation decreases.
Largest safety benefits occur on freeways with adverse weather, downhill grades, tunnels, and bridges.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
6 / 17
Notes: Other statistical analysis performed that didn’t make the paper – underscores these key findings from the literature, and argue most directly for the use of TLR as an approach.
Vehicle Type to Road Conditions: only explain 1.3% of variation, but lower coded (weight) vehicles crash more in adverse conditions, trucks mostly in dry conditions. This data counter to perception actually supports TLR.
Vehicle Type by Time of Day: most accidents happen evening or morning – truck more in evening.
Vehicle Type to Crash Type:

## Slide 8
Crash Data Studies & CDOT's LOSS Map
Place-specific data identifies high-risk segments
CDOT Level of Service of Safety (LOSS) Map — Glenwood Canyon
WHAT THE MAP SHOWS
Three canyon segments rated LOSS Level 4 — "high potential for crash reduction" (the highest category)
Adjacent segments rated LOSS Level 3 — moderate-to-high potential
Roughly half the canyon meets Liu's definition of a "constrained or high-risk corridor"
Methodological precedent
Choi (2019) used a 3-year before / 3-year after framework. With limited canyon-specific data, this project applies a parallel 2-year before / 2-year after design.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
7 / 17
Notes: Background as to why Crash data is compiled. So much information available on CDOT Website, safety priorities, traffic counts, annual reports, projects.
Pause here to mention the Data provided by CDOT Staff – Crash Data and Closure Data
LOSS map – to explain what crash data is collected to do. Visual of how much of the canyon is high risk.

## Slide 9
Why the Literature Supports TLR for Glenwood Canyon
Canyon conditions match the situations where TLRS deliver the most safety benefit
GLENWOOD CANYON CONDITION
WHAT THE LITERATURE SAYS
Tight curves, tunnels, bridges
Choi: largest TLRS safety benefits on segments with tunnels, bridges, downhill grades
Narrow shoulders, constrained geometry
Liu: TLRS most effective in constrained or high-risk corridors
Adverse weather (winter storms, ice)
Choi: speed variation grows under adverse weather — TLRS reduces variation
Traffic 25,800 AADT, ~13.7% trucks
El-Tantawy: TLRS especially effective when truck share exceeds 15% (canyon is close)
Differential capabilities of trucks vs cars
Liu: large vehicles have limited maneuvering and braking — separation reduces hazardous interactions
Conclusion: Glenwood Canyon is precisely the type of corridor where TLR is theoretically most beneficial.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
8 / 17
Notes: What is a literature study? How does your research fit into the field of study, the body of work compiled over time by researchers internationally that is Peer Reviewed? This is a little muddled with Google Scholar and AI these days. References matter. Much of the Statistics study in MPA coursework was intended to prepare discerning eyes for what is trusted, and moreso, what the assumptions are in Statistics, not to make us Data Analysts. I am not that.
Exciting to see your inquiry in that body of academic, practitioner and journalistic study.
Modeling studies mostly on urban freeways- Choi and Liu speak to GW Canyon-type conditions

## Slide 10
Methodology: Quasi-Experimental Before/After
TLR implemented January 1, 2024 — a natural intervention point
BEFORE (Control)
2022 – 2023
263 total crashes | 64 truck-involved
Jan 1, 2024
TLR Implemented
AFTER (Treatment)
2024 – 2025
219 total crashes | 50 truck-involved
FOUR LEVELS OF ANALYSIS
1
Crash Counts
Raw crash totals: trucks vs. all vehicles
2
Traffic Volume
Annual Average Daily Traffic, including truck share
3
Crash Rates
Crashes per Million Vehicle Miles Traveled
4
Inferential Tests
Three Chi-Square + a Poisson rate test
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
9 / 17
Notes: Wanted to start where most drivers would – with counts and averages. Inductive – looking for patterns in the data. HUGE DATA set. Intimidating.
Factor for traffic volume to develop Crash Rates – Methodology.
Small sample size, then parsed by two-year segments and for trucks shows common problem. Differences among groups. No good control group – similar other location. Concerned with historical data.
Made a leap from Descriptive Stats to Deductive analysis. Empirical Bayesian beyond my ability. Could run some frequency tests which required moving to hypotheses

## Slide 11
Descriptive Analysis: KEY DESCRIPTIVE FINDINGS
Chart: 
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
10 / 17

## Slide 12
Descriptive Analysis: KEY DESCRIPTIVE FINDINGS
Each level adds context to compensate for small sample size
Chart: 
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
10 / 17

## Slide 13
Descriptive Analysis: Building from Counts to Rates
Each level adds context to compensate for small sample size
Chart: Truck/Bus % of Total Crashes — Annual & Period Averages
| 2022 | 2023 | Pre-TLR (2022-23) | 2024 | 2025 | Post-TLR (2024-25)
Truck/Bus % of Total Crashes | 21.7 | 26.4 | 24.3 | 18 | 27.8 | 22.8
KEY DESCRIPTIVE FINDINGS
Within the Study Period
13.7%
Trucks as share of overall traffic (AADT)
23.7%
Trucks' share of crashes during the study period
−23.2%
Reduction in truck crash rate per MVMT (pre vs. post)
Source: CDOT crash data; CDOT OTIS traffic counts (Station 000105)
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
10 / 17
Notes: Face Values – look at two year averages in blue vs annual in red, can see challenge with hanging hat on the TLR reduction argument on count.
Cannot answer counterfactual “what if there were no TLRs applied?” Would the trend line of rising historic crashes have continued? Was it blunted?
This is where we must be clear that this is student work. I am not a professional traffic engineer or data analyst. Wanted to begin from what a consumer would see rather than diving right into modeling that was above my head.

## Slide 14
Inferential Tests: Three Chi-Square + Poisson Cross-Check
Each test asks a different question to compensate for limited statistical power
TEST A
Are trucks disproportionately involved in crashes relative to their share of traffic?
H₀: truck crash share = truck traffic share • Method: Chi-Square Goodness-of-Fit
TEST B
Did TLR change the proportion of truck crashes from before to after?
H₀: post-TLR truck crash proportion = pre-TLR proportion • Method: Chi-Square (count-based)
TEST C
Did TLR change the truck crash rate (adjusted for traffic volume)?
H₀: post-TLR truck crash rate per MVMT = pre-TLR rate • Method: Chi-Square (rate-adjusted)
POISSON
Cross-check on Test C: does the rate ratio's confidence interval exclude 1.0?
H₀: rate ratio = 1.0 • Method: Poisson rate test (Wald + exact)
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
11 / 17

## Slide 15
Finding 1 — Trucks Are Overrepresented in Crashes
Test A: Chi-Square Goodness-of-Fit
RESULT
Reject H₀ (Null Hypothesis)
Trucks are statistically disproportionately involved in crashes relative to their share of traffic.
This finding alone supports CDOT's policy attention to trucks as a safety target — and supports continued use of TLR as part of a broader strategy.
TEST STATISTICS
χ² statistic
46.893
Critical value (α=0.05)
9.488
p-value
< 0.001
Degrees of freedom
4
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
12 / 17
Notes: This statistical analysis supports one of paramount aspects of the Research – is the focus on trucks warranted?
Literature supports it, does the data?

## Slide 16
Finding 2 — Mixed Results on TLR Effectiveness
Tests B and C give different answers; the Poisson cross-check straddles the threshold
TEST B
By count: did TLR change truck crash proportion?
χ² = 0.269 p = 0.604
Not significant
Pre-period rate would have predicted ~65 truck crashes post-TLR; only 50 occurred. Total crashes also dropped, which dilutes the proportional difference.
TEST C
By rate (adjusted for traffic volume): did the truck crash rate change?
χ² = 5.011 p = 0.025
Significant
Truck crash rate fell from 2.09 to 1.60 per MVMT — a 23.2% reduction. When traffic volume is accounted for, the change crosses the significance threshold.
POISSON
Cross-check: does the 95% CI for the rate ratio exclude 1.0?
RR = 0.768 95% CI: 0.530 – 1.111
Not Significant
CI lower bound (0.53) is well below 1.0, but upper bound (1.11) crosses 1.0 — fails the strict test. Pooling both periods reduces the Chi-Square's optimism.
Bottom line: 4 years isn't enough data for a clean answer. The reduction is real and meaningful — but not yet statistically robust at every level.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
13 / 17
Notes: This is the place where limited number of years in the study period and the sample size really show up. I would venture that these would move toward alignment over time with more of both which is a good argument for continuing to study TLR in Glenwood Canyon.
Skaug notes that small samples are common and require cautious treatment. Realizing that CDOT will continue to apply applications which may make isolation of TLR more difficult over time also.
Realized today that I am missing a Measurement table in the Appenices.

## Slide 17
Closure Data: Contextual Only
Why the closure data couldn't bear the same analytical weight as crashes
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
14 / 17
Notes: Note that this is covered in the paper in detail, sounds like a lot of caveats: different tools, different counts

## Slide 18
Finding 3 — Closure Data: Contextual Only
Why the closure data couldn't bear the same analytical weight as crashes
WHY THE CLOSURE DATA IS DIFFERENT
CMV ≠ truck
"Commercial Motor Vehicle" doesn't precisely overlay any of CDOT's other truck definitions
Closures span 5 categories
Traffic, crash, environmental, incident, outside agency. TLR can only address some.
No literature precedent
TLR research focuses on crash reduction and flow, not on closure frequency or duration
Different collection methodology
Closure data assembled from camera footage; crash data from State Patrol on-scene reports
CONTEXTUAL FINDINGS (2022–2025)
1,101
total closure incidents
177
CMV-involved (16.1% of closures)
CMV-Involved Closures: Pre vs. Post TLR
Pre-TLR (2022–23): 67 of 482 closures (13.9% CMV)
Post-TLR (2024–25): 110 of 619 closures (17.8% CMV)
“Closure data does not show TLR reduced CMV-involved closures — but most closures are non-crash events that TLR was never expected to address.”
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
14 / 17
Notes: Note that this is covered in the paper in detail, sounds like a lot of caveats: different tools, different counts

## Slide 19
Conclusions from the Data
What the four years of Glenwood Canyon data warrant — and what they do not
The disproportion of crashes involving trucks is established;
that TLRs caused a reduction is plausible but not yet proven.
Across four years and 482 crashes, trucks are statistically over-represented in Glenwood Canyon crashes relative to their share of traffic (Test A: χ²=46.9, p<0.001). The post-TLR truck crash rate fell 23.2% per MVMT — directionally consistent with the literature — but this short window of data straddles the statistical-significance threshold. The data warrants continued use of TLR; it does not yet warrant a definitive causal claim.
Operational, data-driven interventions vs major infrastructure improvements are the only realistic path forward.
Structurally re-engineering Glenwood Canyon, or building parallel capacity, is unlikely given cost-benefit constraints. That reality elevates low-cost, evidence-based operational tools — TLR among them — as the most viable instruments for managing truck-related risk on this corridor. The closure problem and the crash problem cannot be addressed in isolation.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
16 / 17

## Slide 20
Conclusions
What the four years of Glenwood Canyon data warrant — and what they do not
Studying Crash Data (and perhaps Closure Data) in GWC can be done with someone willing to take the time to clean and align the two datasets to more accurately assess the impact of TLR or other interventions.
CDOT collects the data. What is CDOT’s role in employing that data for various policy analysis?
There is crash data back to 2007. Another 2-5 years of data collection would begin to refine the hypotheses, and inform both operational practice, and perhaps temper the urge to rush to legislation before collecting data.
Modeling shows that there is much more data that could be collected in this segment if desired. That is likely true of Vail Pass and the Twin Tunnels from both directions. For one, there is extensive actual weather data that could inform
What other interventions will be implemented next, and can they be set up with monitoring protocols to help refine the closure practices and determine which human causes need to be addressed with interventions?
What about in-vehicle data collection? Infrastructure to Vehicle Collection?
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
16 / 17

## Slide 21
Overall Recommendations
Truck lane restrictions are a low-cost intervention with measurable safety value
✓
Maintain TLR as part of a broader strategy
Trucks are disproportionately involved in crashes (Test A). The post-TLR rate reduction, while not robust at every test, is real and aligns with literature. Cost of installation under $30,000 makes the intervention defensible even with modest evidence.
↗
Invest in better data infrastructure & engage I-70 Coalition as a partner
Reconcile classification systems across CDOT crash, traffic, and closure data. Build a CMV-to-crash crosswalk so future analyses can directly link closures to specific events. Consider emerging telematics.
→
If proving TLR statistical validity matters, expand the research design
Approach a follow-on study that adds a qualitative element — interviewing drivers about their experience in the canyon. Run regression models that isolate possible external factors such as weather and other road conditions. And run the same significance tests in coming years as more data accumulates beyond the four-year study window.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
15 / 17

## Slide 22
Recommendations for I 70 Coalition
✓
Consider Partnering with CDOT in Data Analysis
CDOT will continue to collect robust data sets. Public and local leadership push to implement some intervention regarding trucks after the winter of 2023 shows that the agency is responsive to pressure, but more data-driven responses could result in backing the agency in projects that require additional funding or political will.
↗
Extend Data Study Area and Scope
Study on Vail Pass or Eisenhower Pass would likely confirm CDOT’s metering and rapid closure policies but might not support applying TLR throughout the corridor.
Encouraging more low-cost pilot interventions could result in improved traffic flow.
→
Careful to not Scapegoat Truckers
Sixty eight percent of accidents involving trucks occur on dry roads, and at or below the speed limit.
Increasing fines on truckers is of limited value (but do a study on that), but trucker behavior can be modified.
Changing trucking practices, modifying driving behavior may require cooperation with industry.
Just because this project shows that trucks are “disproportionately involved” in accidents, doesn’t imply that trucks are the “cause” of those accidents.
Stavney | Truck Lane Restrictions in Glenwood Canyon | UC Denver SPA Capstone, Spring 2026
15 / 17

## Slide 23
QUESTIONS & DISCUSSION
Thank You
WITH SPECIAL THANKS TO
CDOT Region 3 Staff
Drewe Lee, Trevor Allen, Jason Smith
Professor Todd Ely
Capstone Instructor, UC Denver SPA
Professor Propheter
Second Reader, UC Denver SPA
Jonathan Godes
Executive Director, I-70 Coalition
The I-70 Coalition
Project client
Jon Stavney • UC Denver School of Public Affairs • Spring 2026 Capstone • May 1, 2026